## Slide 1
STORAGE TECHNOLOGY
RAID
Redundant Array of Independent Disks
Jelena Matijaš, 1102/23

## Slide 2
TABLE OF CONTENTS
01
Introduction
Why RAID? The need for storage solutions
02
RAID 0 — Striping
Performance at the cost of redundancy
03
RAID 1 — Mirroring
Reliability through data duplication
04
RAID 5 & 6
Balanced performance, capacity & safety
05
RAID 0+1, 1+0 & JBOD
Hybrid and combined approaches
06
Conclusion
Summary and choosing the right RAID level

## Slide 3
INTRODUCTION
The Problem
A single storage device often cannot meet all performance, capacity, or reliability requirements.
Some specs simply don't exist — e.g., no single HDD offers 200 TB today.
High-performance single disks (SLED) are extremely expensive.
Single points of failure put critical data at risk.
The Solution: RAID
RAID (Redundant Array of Independent Disks) is a storage virtualization technique that combines multiple physical drives into one logical unit.
↑ Performance
↑ Capacity
↑ Reliability
↓ Cost per GB
vs. SLED: Single Large Expensive Disk — RAID's predecessor and antithesis.

## Slide 4
RAID 0 — Striping
Disk 1
Stripe 1
Stripe 5
Stripe 9
Disk 2
Stripe 2
Stripe 6
Stripe 10
Disk 3
Stripe 3
Stripe 7
Stripe 11
Disk 4
Stripe 4
Stripe 8
Stripe 12
Data distributed across all disks in parallel
⚡ Performance
Up to 4× faster reads & writes (N disks)
💾 Capacity
Full sum of all disk capacities
⚠️ Reliability
Zero fault tolerance — one disk failure = total data loss
🔢 Minimum
2 disks required
⚠ Performance is bought with reliability

## Slide 5
RAID 1 — Mirroring
Primary
Block A
Block B
Block C
Block D
Mirror 1
Block A
Block B
Block C
Block D
Mirror 2
Block A
Block B
Block C
Block D
→ COPY →
→ COPY →
🛡️ Reliability
Survives failure of N-1 disks — data safe as long as one disk works
⚡ Performance
Writes: no gain. Reads: up to N× faster in some implementations
💾 Capacity
Equal to a single disk — all others are mirrors
🔢 Minimum
2 disks required
✓ Reliability is bought with capacity

## Slide 6
RAID 5 & 6 — Distributed Parity
RAID 5
D1
A1
B1
C1
P(D)
D2
A2
B2
P(C)
D1
D3
A3
P(B)
C2
D2
D4
P(A)
B3
C3
D3
Parity (XOR)
Parity rotates across all disks equally
Tolerates 1 disk failure
Capacity = N−1 disks
Min. 3 disks
Best for large sequential I/O (backups)
Not ideal for many small random writes
RAID 6
Same as RAID 5 but with two independent parity blocks per stripe, spread across all disks.
Fault Tolerance:
Survives 2 simultaneous disk failures
Capacity:
N−2 disks of usable space
Minimum Disks:
4 disks required
Best Use Case:
Large arrays where rebuild time is long
Why Not RAID 5?:
Long rebuild = high risk of second failure during rebuild

## Slide 7
RAID 0+1, 1+0 & JBOD — Hybrid Levels
RAID 0+1 (Mirror of Stripes)
D1
Str1
Str3
Str5
D2
Str2
Str4
Str6
D3
Str1
Str3
Str5
D4
Str2
Str4
Str6
⟺ MIRROR
• If one disk fails → degraded RAID 0 on that side
• If second failure is on the SAME side → data loss
• Less fault-tolerant than RAID 10
RAID 1+0 (Stripe of Mirrors)
• Survives any single disk failure
• Can survive multiple failures if not in same mirror pair
• Preferred over RAID 0+1 in practice
• Min. 4 disks | Capacity = N/2
JBOD — Just a Bunch of Disks
Simple concatenation of disks. No performance gain; partial fault recovery possible as most files fit on one disk.
D1
Str1
Str3
Str5
D2
Str1
Str3
Str5
D3
Str2
Str4
Str6
D4
Str2
Str4
Str6

## Slide 8
CONCLUSION
Choosing the Right RAID Level
RAID 0
Need maximum speed; data loss is acceptable (temp/scratch)
RAID 1
OS drives or critical low-volume data requiring high redundancy
RAID 5
General purpose servers with large, sequential workloads
RAID 6
Large arrays or critical data where RAID 5 rebuild risk is too high
RAID 0+1 | RAID 1+0
Databases & high-transaction systems needing both speed AND redundancy
Key Insight: No single RAID level is universally best. Every level trades off performance, capacity, and reliability. Match the level to your workload, budget, and risk tolerance.

## Slide 9
Thank you!